## Slide 1
Setup for simulations
2022-09-08

## Slide 2
Use case simulation workflow
Steps
Download wind data, city data and separation lookup tables
Create city graph
Create flight plan CSV (only for delivery and background)
Preprocess wind scenario
Fill out configuration file
  Select path to city graph created
  Select path to CSV file containing flight plans
  Select paths to surveillance and emergency drones pre-defined scenarios (Indra)
  Select paths to lookup tables and wind data
Run USEPE plugin in BlueSky
Post-process raw results obtained (USEPE logger, statelog)

## Slide 3
Use case simulation workflow
Data to download
These data are too large to check into Github, so they are stored on ISDEFE’s Sharefile.
1. Download city data from Sharefile: WP 4 > T 4.1 > 03 Building data > Hannover > CityGML_LoD1 and place it for example in "/home/oda/ws/building_data"
2. Download wind data from Sharefile: WP 4 > T 4.1 > 00 Wind field > scenario_3 and place the files in bluesky/usepe/segmentation_service/data/wind/exercise_3
3. Download separation lookup tables from Sharefile: WP 4 > T 4.1 > 04 Separation volumes and place the files in scenarios/exercise_3/data/lookup_tables
(Replace «3» with the number of your exercise)

## Slide 4
Create city graph
Create graph
Define in your configuration file (.cfg) the parameters required for the solution scenario:
  Define city latitude and longitude of the region of interest (in both [City] and [BuildingData] sections)
  Define number of layers of the graph and spacing between them (remember discussion VLL)
  Select import = False in [City] section
  Include the corridor numbers (1, 2, 3, 4) to include them in the graph
  Select altitude of the first corridor and distance with the second
  Select path to the building data (directory_hannover)
  Select name and location of the graph generated (graph_path in [Outputs])
Run exercise_1_graph_creation.ipynb. It will create the graph of the city in the data folder. It will take some time (in our case around 30 minutes).
  Jupyter notebook located in GitHub USEPE organization’s scenario repository

## Slide 5
Config file example
[City]
mode = rectangle
# hannover_lat = 52.376
# hannover_lon = 9.76
# zone_size = 1000
hannover_lat_min = 52.297839999994714
hannover_lat_max = 52.438260000005286
hannover_lon_min = 9.643080000001035
hannover_lon_max = 9.844349999998968
import = False
imported_graph_path = ./data/exercise_1_reference.graphml
[Layers]
number_of_layers = 8
layer_width = 15
[BuildingData]
lat_min = 52.297839999994714
lat_max = 52.438260000005286
lon_min = 9.643080000001035
lon_max = 9.844349999998968
divisions = 20
directory_hannover = C:\workspace3\bluesky_usepe_git\usepe\city_model\data\CityGML_LoD1
[Options]
one_way = False
simplify = True
simplification_distance = 0
simplification_error = 2
[Outputs]
graph_path = ./data/test_corridors.graphml
[Corridors]
corridors = 1, 2, 3, 4
altitude = 135
delta_z = 15
speed = 50
acceleration_length = 50
file_path_corridors = ./data/usepe-hannover-corridors.geojson

## Slide 6
Create flight plan CSV
Create flights CSV
Change the option import = True in the your config file (.cfg) and make sure that the path imported_graph_path = ./data/exercise_1_reference.graphml has the same name as the graph created.
Open the case_study_csv_file_generator.ipynb notebook. Note the first box in which you should specify the path where you have checked out the BlueSky repository and the scenarios repository (path to the local folder in which the notebooks are).
It has a function to create the CSV file of background traffic and another function to create CSVs for each operational scenario of the delivery use case. It is possible to give inputs to the background traffic function:
  Density: you can select between the 3 predefined values or include a new one
  Average flight duration: in seconds
  Simulation total time: in seconds (7200s)

## Slide 7
Create wind scenario
Create wind scenario
Use bluesky/usepe/wind/wind_preprocess.py
Define path to wind data file and granularity for the interpolation in the scenarios
path = Path( "./data/USEPE_S1_3d_nest01.nc" )
grid_spacing_list = [5, 10, 20]

## Slide 8
Run USEPE plugin
Run scenario
Define all the paths and parameters required in the config file
Create folder usepe/temp in bluesky/scenario in your computer
Download from sharefile the different files required
  Look up tables folder
  Wind file of your scenario
  Reference parameters ([BlueSky] configuration_path)
Run BlueSky
Run the USEPE plugin
  00:00:00.00 > PLUGIN USEPE
  00:00:00.00 > USEPE CONFIG {config path}
  00:00:00.00 > USEPE ON